Two projects to
optimize Python
FOSDEM 2013, Bruxelles
Victor Stinner
<victor.stinner@gmail.com>
Distributed under CC BY-SA license: http://creativecommons.org/licenses/by-sa/3.0/

---
Agenda
- CPython bytecode is inefficient
- AST optimizer
- Register-based bytecode

---
Part I
CPython bytecode
is inefficient

---
CPython is inefficient
- Python is very dynamic, cannot be easily optimized
- CPython peephole optimizer only supports basic optimizations like replacing 1+1 with 2
- CPython bytecode is inefficient

---
Inefficient bytecode
Given a simple function:
def func():
   x = 33
   return x

---
Inefficient bytecode
- I get:
  (4 instructions)
- I expected:
  (2 instructions)
- Or even:
  (1 instruction)
LOAD_CONST 1 (33)
STORE_FAST 0 (x)
LOAD_FAST 0 (x)
RETURN_VALUE
LOAD_CONST 1 (33)
RETURN_VALUE
RETURN_CONST 0 (33)

---
How Python works
  - Parse the source code
  - Build an Abstract Syntax Tree (AST)
  - Emit Bytebyte
  - Peephole optimizer
  - Evaluate bytecode

---
Let's optimize!
  - Parse the source code
  - Build an Abstract Syntax Tree (AST)
    → astoptimizer
  - Emit Bytebyte
  - Peephole optimizer
  - Evaluate bytecode
    → registervm

---
Part II
AST optimizer

---
AST optimizer
- AST is high-level and contains a lot of information
- Rewrite AST to get faster code
- Disable dynamic features of Python to allow more optimizations
- Unpythonic optimizations are disabled by default

---
AST optimizations (1)
- Call builtin functions and methods:
  len("abc") → 3
  (32).bit_length() → 6
  math.log(32) / math.log(2) → 5.0
- Evaluate str % args and print(arg1, arg2, ...)
  "x=%s" % 5 → "x=5"
  print(2.3) → print("2.3")

---
AST optimizations (2)
- Simplify expressions (2 instructions => 1):
  not(x in y) → x not in y
- Optimize loops (Python 2 only):
  while True: ... → while 1: ...
  for x in range(10): ...
  → for x in xrange(10): ...
  In Python 2, True requires a (slow) global lookup, the number 1 is a constant

---
AST optimizations (3)
- Replace list (build at runtime) with tuple (constant):
  for x in [1, 2, 3]: ...
  → for x in (1, 2, 3): ...
- Replace list with set (Python 3 only):
  if x in [1, 2, 3]: ...
  → if x in {1, 2, 3}: ...
  In Python 3, {1,2,3} is converted to a constant frozenset (if used in a test)

---
AST optimizations (4)
- Evaluate operators:
  "abcdef"[:3] → "abc"
  def f(): return 2 if 4 < 5 else 3
  → def f(): return 2
- Remove dead code:
  if 0: ...
  → pass

---
Used as a preprocessor
- "if DEBUG" and "if os.name == 'nt'" have a cost at runtime
- Tests can be removed at compile time:
  cfg.add_constant('DEBUG', False)
  cfg.add_constant('os.name',
          os.name)
- Pythonic preprocessor: no need to modify your code, code works without the preprocessor

---
astoptimizer TODO list
- Constant folding: experimental support (buggy)
- Unroll (short) loops
- Function inlining (is it possible?)

---
Part III
Register-based
bytecode

---
registervm
- Rewrite instructions to use registers instead of the stack
- Use single assignment form (SSA)
- Build the control flow graph
- Apply different optimizations
- Register allocator
- Emit bytecode

---
Stack-based bytecode
def func():
   x = 33
   return x + 1
LOAD_CONST 1 (33) # stack: []
STORE_FAST 0 (x) # stack: [33]
LOAD_FAST 0 (x) # stack: []
LOAD_CONST 2 (1) # stack: [33]
BINARY_ADD # stack: [33, 1]
RETURN_VALUE # stack: [34]
(6 instructions)

---
Register bytecode
def func():
   x = 33
   return x + 1
LOAD_CONST_REG 'x', 33 (const#1)
LOAD_CONST_REG R0, 1 (const#2)
BINARY_ADD_REG R0, 'x', R0
RETURN_VALUE_REG R0
(4 instructions)

---
registervm optim (1)
- Using registers allows more optimizations
- Move constants loads and globals loads (slow) out of loops:
  return [str(item) for item in data]
- Constant folding:
  x=1; y=x; return y
  → y=1; return y
- Remove duplicate load/store instructions: constants, names, globals, etc.

---
Merge duplicate loads
Stack-based bytecode :
return (len("a"), len("a"))
LOAD_GLOBAL 'len' (name#0)
LOAD_CONST 'a' (const#1)
CALL_FUNCTION (1 positional)
LOAD_GLOBAL 'len' (name#0)
LOAD_CONST 'a' (const#1)
CALL_FUNCTION (1 positional)
BUILD_TUPLE 2
RETURN_VALUE

---
Merge duplicate loads
Register-based bytecode :
return (len("a"), len("a"))
LOAD_GLOBAL_REG R0, 'len' (name#0)
LOAD_CONST_REG R1, 'a' (const#1)
CALL_FUNCTION_REG R2, R0, 1, R1
CALL_FUNCTION_REG R0, R0, 1, R1
CLEAR_REG R1
BUILD_TUPLE_REG R2, 2, R2, R0
RETURN_VALUE_REG R2

---
registervm optim (2)
- Remove unreachable instructions (dead code)
- Remove useless jumps (relative jump + 0)

---
Pybench results
- BuiltinMethodLookup:
  fewer instructions: 390 => 22
  24 ms => 1 ms (24x faster)
- NormalInstanceAttribute:
  fewer instructions: 381 => 81
  40 ms => 21 ms (1.9x faster)
- StringPredicates:
  fewer instructions: 303 => 92
  42 ms => 24 ms (1.8x faster)

---
Pybench results
- Pybench is a microbenchmark
- Don't expect such speedup on your applications
- registervm is still experimental and emits invalid code

---
Other projects
- PyPy and its amazing JIT
- Pymothoa, Numba: JIT (LLVM)
- WPython: "Wordcode-based" bytecode
- Hotpy 2
- Shedskin, Pythran, Nuitka: compile to C++

---
Questions?
https://bitbucket.org/haypo/astoptimizer
http://hg.python.org/sandbox/registervm
Contact:
victor.stinner@gmail.com
Distributed under CC BY-SA license: http://creativecommons.org/licenses/by-sa/3.0/

---
Thanks to David Malcom
for the LibreOffice template
http://dmalcolm.livejournal.com/